## Slide 1: SABO Garbage Collection Trolley

## Slide 2: Model 1.0
Primary design shown at Dassault Systems

## Slide 3
Rotating brush that will throw garbage inside
E.T. Kapusawala shop
Contact no :9890126823
Conveyor for lifting garbage to pre-collection area
Pre-collection area
Operator will do manual segregation of dry garbage and wet garbage by hand with gloves
Dry Garbage
Wet Garbage
Path of garbage
Full covered body for stopping formation of dust clouds

## Slide 4
Chain drive for transmission.
Gear sprockets for speed reduction
Space for battery and motor

## Slide 5: Model 2.0
Unique design for garbage collection with two Rotor system
Simple in design and Smaller in size
Less mechanical components and less cost
Easy for maintenance

## Slide 6
We have completed modelling and weldments for this design as we have already shared the same with you.
Also we have done calculations for brush and drum arrangement, selection of motor, speed calculations for brush and drum, chain drive transmission for achieving the same, etc.

## Slide 7
Two rotor system
Battery and motor palcement
Throw of garbage is tangential to second rotor with projectile path
Path of garbage

## Slide 8: Model 3.0

## Slide 9
Rotating brush that will throw garbage inside
E.T. Kapusawala shop
Contact no :9890126823
Conveyor for lifting garbage to pre-collection area
Pre-collection area
Operator will do manual segregation of dry garbage and wet garbage by hand with gloves
Dry Garbage
Wet Garbage
Same as
model 1.0
but with
additional features

## Slide 10
ADDITIONAL FEATURES
Conveyor transition plates with teethes which will separate sand and garbage
Separate sand container
Simple drawer type arrangement for removing sand
Vibration because of road surface roughness causes soil to move on slope
Comb for cleaning brush on every rotation

## Slide 11
We have taken the decision to start working on model 3.0
We want your opinion on :
Should we continue model 2.0 as it is simple and don't have more mechanical components as Gadgil sir told during session start with simple model or we should work on model 3.0 with more features and full functionality ?
MODEL 3.0
More features
Complex design than 2.0
Simple manufacturable parts
We know we have already wasted time but we can work on model 3.0 and can give you more better outcomes in upcoming days .We will update you daily .
MODEL 2.0
Less features
Simple design
Parts with complex profiles
We have already completed most designing and calculation part. WE have time but there is limitation to start making prototype